## Slide 1: Flight Software & SITL Architecture
Review date
10 October 2026
Program
Compact Delivery Quad
Q4 2026
Hackathon Project
Notes: Source: repository README.md, docs/ARCHITECTURE.md and docs/TEST_RESULTS.md. This deck describes the software/SITL prototype and its limits; it is not a flight-readiness assessment.

## Slide 2: SITL system architecture
01 Companion policy
Authenticates requests, validates route, health and return reserve, then uploads the mission. Recovery requests are limited to RTL or LAND.
02 ArduCopter SITL
Local 4.6.3 stock X-quad model owns dynamics and flight-controller failsafes; MAVLink telemetry feeds the companion and test logger.
03 Sensors + evidence
GNSS, range, camera and payload interlocks are synthetic. Fault injection and JSONL/DataFlash logs support review; release stays in-memory.
Loopback-only test: companion and ArduCopter SITL run on the host; synthetic observations and local logs close the loop. Nothing connects to a physical aircraft.
Notes: Sources: docs/ARCHITECTURE.md; flight-software/quadstack/core.py, service.py and delivery.py. The state gates and mission checks describe implemented policy behavior.

## Slide 3: Flight-control responsibilities
Pixhawk 6C • ArduCopter
Owns stabilization, state estimation, motor mixing, arming checks, navigation and flight modes.
Executes AUTO missions and geofence
Owns battery, RC and GCS failsafes
Accepts bounded RTL / LAND recovery
Pi Zero 2 W • Python companion
Authenticates requests; validates route, state, health and return margin.
Reports health and mission status
Optional image-only fiducial input
No arm, motor, servo or parameter API
Boundary rule
ArduCopter remains the flight and safety authority. The companion may upload a validated mission or request RTL/LAND recovery; the operator explicitly starts every SITL flight.
Payload actuation is an in-memory mock, gated by explicit SITL opt-in; no servo or gripper command is sent.
Notes: Sources: README.md; simulation/transport.py; simulation/version-manifest.json. SITL uses ArduCopter 4.6.3 with an unmodified stock X-quad dynamics model (3 kg, 350 mm, 3S), not selected-aircraft dynamics. Sensor observations are synthetic where noted; simulated release is in-memory only.

## Slide 4: SITL evidence and model limits
152 distinct checks passed across two runs: 143 full-suite checks and 9 bridge checks. SITL validates software behavior; the selected aircraft’s performance is not validated.
Evidence | Coverage | Result | Setup | Limit
Policy + API | 132 checks | PASS | Unit / HTTP | No hardware
Delivery faults | 14 flights | PASS | RTL/LAND + mock | Stock quad
Local navigation | 1 round trip | PASS | SITL | Not GPS accuracy
Geographic routes | 3 routes | PASS | WGS84; 0.92–1.45 km | Cargo retained
Bridge | 9 checks | PASS | Custom GPS | Separate run
FC boundary | 37 params | PASS | Upload disarmed | SITL only
Dynamics model | Stock X: 3 kg / 350 mm / 3S | Baseline | Study: 5.70 kg / 650 mm / 6S | Not modeled
Payload output | In-memory mock | Opt-in | No servo command | No reliability proof
Notes: Source: docs/TEST_RESULTS.md and docs/test-evidence.json. The 143 full-suite checks and 9 bridge checks were separate runs (152 distinct checks in total). The table states the tested scope and principal model limits.

## Slide 5: Next validation gates
Airframe fidelity
Fit the model to verified 5.70 kg, 650 mm, 16 in and 6S data before making performance claims.
Sensor fidelity
Confirm interface, mounting, timing and calibration; add measured noise and dropout profiles.
Bench readiness
Review wiring and failsafes on a prop-off bench; physical actuation needs an approved test procedure.
Gate 1
Gate 2
Gate 3
Notes: Open validation gates are proposed from the documented model and hardware gaps. No schedule or physical-flight readiness date is claimed.